## Slide 1: Hands-On Groundwater Modeling: Supplementary Material Randolf Rausch & Anneli Guthke

## Slide 2: Contents

## Slide 3: Remarks on flow equation
The groundwater flow equation is a diffusion equation (1-D):
Diffusivity:
Diffusion leads to a reduction of concentration differences. In the beginning, the propagation is very fast. Then, it becomes slower, as the gradient decreases. That means the driving force decreases.
Compare with Fick’s second law

## Slide 4: Diffusion time and velocity
D = Diffusion time: t =
Diffusion velocity (derivative distance time):
Propagation velocity in an aquifer:
  𝑣 increases with increasing T
  𝑣 increases with decreasing S
=

## Slide 5: Example
Example for the calculation of diffusion time:
  Given: Distance L = 1 m, Diffusion coefficient D = 1∙ 10-9 m2/s
  Wanted: Diffusion time
t = = = 1∙109 s = 31.7 years

## Slide 6: Propagation times
Diffusive propagation time:
Advective propagation time:
The ratio of diffuse to advective propagation time is called Peclet number. The Peclet number (Pe) is a dimensionless number.
Pe = 0, pure dispersive transport
Pe = ∞, pure advective transport
tdiffusive =
tadvective =
with:
L = length
D = diffusivity
u = pore velocity
Pe = = = = = =

## Slide 7: Simulation of well drawdown
Comparison of computed and observed head within a cell
Note: Well loss!
Finite difference grid
Simulated head distribution

## Slide 8: Simulation of wells in 3-D-model
Grid refinement in horizontal direction
Distribution of total discharge to different layers:
Proportional to transmissivity of layer
Total discharge in 1 cell, but high vertical hydraulic conductivity in well cells
Falling dry of nodes leads to instabilities! Way out: adjustment of pumping rate

## Slide 9: Radial model approach
Model grid
Simulated head distribution
Radial flow to a well
Aquifer thickness: m = U = 2 ∙ π ∙ r
Transmissivity: T = U ∙ K = 2 ∙ π ∙ r ∙ K
Storage coefficient: S = U ∙ S0 = 2 ∙ π ∙ r ∙ S0

## Slide 10: Advantages of radial approach
Anisotropy
Kx > Kz
Layering
Imperfect well
Arbitrary location of well screen

## Slide 11: Well storage
Wells can store a big amount of water which will be extracted at the begin of pumping test before aquifer discharge starts

## Slide 12: Skin effect

## Slide 13: Unconfined (“phreatic”) aquifer
Note: There is no analytical solution for the unconfined aquifer!
Approximations are only valid:
If drawdown is small compared to aquifer thickness,
and Dupuit assumptions are full filled
Free water surface (h = z) or seepage line
Seepage face

## Slide 14: Pathlines and Flowlines
Definition of streamline, pathline, and flowline:
Streamline
Pathline/flowline

## Slide 15: Velocities
Darcy velocity vf
  Relevant for mass balances:
  The Darcy velocity is related to the total cross sectional area.
Pore velocity u (seepage or average linear velocity)
  Relevant for transport time:
  The pore velocity is restricted to the effective cross section. Therefore it is larger than the Darcy velocity by the factor 1/nf.

## Slide 16: Velocities
Real velocity vr: ?
Pore velocity u
Darcy velocity vf (discharge per area)

## Slide 17: Computation of pathlines
Given: pore velocity u
Wanted: displacement s by integration over time

## Slide 18: Computation of pathlines
Integration:
Decompose in velocity components ux and uy
x(t + ∆t) = x(t) + ux ∆t
y(t + ∆t) = y(t) + uy ∆t
Integration methods:
e.g. Euler, Heun, Runge-Kutta
Step correction!

## Slide 19: Velocity interpolation in numerical models
What we need is a continuous velocity field!
Finite Differences:
  Velocities are determined from fluxes between adjacent cells.
  Given vfx and vfy (and vfz) between nodes.
  2 approaches: Prickett- and Pollock-method.
Finite Elements:
  Velocities are determined from derivations of the head distributions and element properties. The velocity is constant in every element.

## Slide 20: Prickett’s method
Velocity interpolation after Prickett et al. (1981).

## Slide 21: Pollock’s method
Given: Flow distribution along cell boundary. No sinks and sources in the interior.
Pathline: For point of entry the point of exit follows immediately from continuity. Interpolation between the points is made on the basis of linear interpolation of velocities vx in x-direction vy in y-direction. Analytical solution exists.

## Slide 22: Comparison: Prickett’s and Pollock’s method

## Slide 23: Drawdown and velocity distribution near a pumping well
Static water level
(pre-pumping)
Water level after
1000 minutes
pumping)
Velocity divide at
177 ft. downgradient
Distance upgradient, ft. Distance downgradient, ft.
Arbitrary elevation, ft.
Vertical cross section around a pumping well

## Slide 24: Numerical computation of isochrones
Idea: Backward tracking

## Slide 25: Solute Transport Modeling
Literature:

## Slide 26: Why solute transport models?
The objective of solute transport models is the quantitative description of contaminants in groundwater

## Slide 27: Motivation
Groundwater transports dissolved substances
The solutes determine the quality of groundwater
The knowledge of transport processes of solutes is important for predicting the spread of a pollutant
Transport provides information on groundwater flow
The knowledge of transport processes is the basis for groundwater protection

## Slide 28: Application of solute transport models
Interpretation of concentration data
Mass balance of contaminants
Predictions of pollutant plumes
Design of pump and treat management
Planning of monitoring strategy
Risk assessment in case of waste disposals

## Slide 29: Example: Thermal plume from nuclear power plant

## Slide 30: Example: Simulation of a contamination plume

## Slide 31: Pollutants
Biological contamination
  Bacteria, viruses …
Inorganic pollutants
  Nitrate
  Heavy metals (e.g. lead, cadmium, mercury, arsenic ...)
  Radio nuclides
Organic pollutants
  Oil products
  Chlorinated hydrocarbons (e.g. tetrachlorethene, trichlorethene, ...)
  Aromatic hydrocarbons (e.g. benzene, toluene, xylene, ...)
  Polycyclic aromatic hydrocarbons (e.g. naphthalene, ...)
  Pesticides (diverse chemical compounds, e.g. atrazine, ...)
  Pharmaceutical residues

## Slide 32: Risk of pollutants
Produced in big quantities
Persistent (no decay)
High solubility
Nonabsorbent (high mobility)
Toxic

## Slide 33: Representation of transport processes
Advection
Advection + Dispersion (+ Diffusion)
Advection + Dispersion + Adsorption
Advection + Dispersion + Adsorption + Decay
Transport in 1-D-aquifer

## Slide 34: Transport mechanisms
Advection
  Dissolved solids are carried along with the average velocity of flowing groundwater
Molecular diffusion
  Transport by concentration gradients (Fick’s law)
Dispersion
  Spreading of pollutants due to heterogeneity of flow field (small scale dispersion, macro dispersion)
Adsorption
  Adsorption of pollutants onto the surfaces of the mineral grains in the aquifer
Chemical and biochemical reactions
  Chemical and biological decay and transformation processes
Radioactive decay in case of radioactive substances

## Slide 35: Advection
Displacement of pollutants in the average direction of groundwater flow
Advective pollutant flux through unit area vertical to flow direction
Note: Convection = motion of fluids due to temperature and density gradients

## Slide 36: Molecular diffusion
Solvent moves by concentration gradient. Transport due to Brownian molecular motion.
Diffuse pollutant flux (Fick´s 1st law)
taking into account the effective flow area
,
,
For u > 0.1 m/d diffusive flux can usually neglected!

## Slide 37: Tortuosity
In a porous medium diffusion is not as effective as in open water. Solute only moves through pores.

## Slide 38: Causes for velocity variations at various spatial scales
2 kinds of dispersion: micro dispersion and macro dispersion (small & large scale)

## Slide 39: Micro dispersion

## Slide 40: Impact of macro dispersion
Pollutant distribution at t = 0
Pollutant distribution at t = t1 > 0

## Slide 41: Physical description of transport by dispersion
Working hypothesis: Description by Fick‘s law in analogy to diffusion
But: The dispersion coefficient is larger than the diffusion coefficient,
And dispersion is always anisotropic => dispersion tensor.

## Slide 42: Dispersion model
resp.
,
,

## Slide 43: Dispersive vs. diffusive transport
Diffusion takes place without flow.
Dispersion takes place only with flow. It results from local deviations of the average groundwater flow.
Dispersion describes the influence of the unknown small scale variations of the flow field. If it was known explicitly, advection and diffusion would be enough for the description of transport processes in groundwater.
Diffusion is isotropic while dispersion is always anisotropic.

## Slide 44: Scale dependence of longitudinal dispersivity
Beims (1983)

## Slide 45: Scale dependence of longitudinal dispersivity
Gelhar et al. (1985)

## Slide 46: Scale dependence of transverse dispersivity
Horizontal transverse dispersivity
Vertical transverse dispersivity

## Slide 47: How can we explain the scale effect of dispersion?
At small scale (lab scale) dispersion due to diffusion, pore size distribution and pore size geometry.
Tortuosity and microscopic variations within a pore and between pores.
At field scale dispersion due to variations in stratigraphy, lithology, and permeability.
Heterogeneity in K and nf

## Slide 48: Scale dependence of longitudinal dispersivity
αL is a measure of the heterogeneity and correlation length of a porous medium
αL >> αT
Laboratory experiments: αT/αL ≈ 0.1
Field studies: αT/αL from 0.001 to 0.3

## Slide 49: Transport fluxes
Flux by:
Advection:
Diffusion:
Dispersion:
Total flux:

## Slide 50: Transport equation
Temporal change in conc. Advection Diffusion Dispersion Sources and
sinks
Solution 2-D: c = f (x, y, t)
Required for solution:
Initial and boundary conditions

## Slide 51: Transport equation
More complex version of the transport equation
Input data:
  Flow field: u(x, y, z, t)
  Transport parameters: nf, D (αL, αTh, αTv, Dm), R, λ
Storage
Advection
Dispersion
Decay
External Sinks/Sources
Retardation

## Slide 52: Remarks on transport equation
Measure for the relation advective/dispersive transport is given by the Peclet number:
  L: typical length scale of transport problem
  Pe = 0 pure dispersive transport
  Pe = ∞ pure advective transport
Notes: Die Transportgleichung ist eine hyperbolische DGL. Unter Vernachlaessigung des Advektionsterms geht die Transportgleichung in eine parabolische DGL ueber. Sie ist dann vom gleichem Typ wie die Stroemungsgleichung.
D d2h/dx2 = dh/dt mit D = T/S (Diffusivitaet des Aquifers).
Ausbreitungszeit advektiver Transport: tA = L/u
Ausbreitungszeit dispersiver Transport: tD = L2/D
Somit folgt fuer Pe = tD/tA, d.h. Pe ist das Verhaeltnis der dispersiven zur advektiven Ausbreitungszeit!

## Slide 53: Remarks on transport equation
The transport equation is a hyperbolic PDE.
Neglecting the advective term the transport equation becomes a parabolic PDE.
Then it is of the same type as the flow equation.

## Slide 54: Boundary and initial conditions
Physical meaning
1st type: specifies advective flux over boundary.
2nd type: specifies diffusive/ dispersive flux over boundary.
3rd type: specifies total flux over boundary.
Initial conditions: Concentration distribution c (x, y, z, t) at time t0

## Slide 55: Choice of boundary conditions
If model area is large enough to contain the total plume: 1st type boundary everywhere (c (boundary) = 0).
At impervious boundaries: 2nd type boundary: dc/dn (boundary) = 0.
Transmission boundary: Extrapolate gradient beyond boundary.

## Slide 56: Boundary conditions (continued)
1st type: c on boundary is given. Specifies advective flux over boundary
2nd type: on boundary is given. Specifies diffusive/ dispersive flux over boundary (often used for impervious boundaries!)
3rd type: on boundary is given. Specifies total flux over boundary
Transmission boundary: D = 0 on boundary
C = 0
impervious
transmission
impervious
1st or 2nd type boundary

## Slide 57: Initial conditions
Concentration distribution c (x, y, z) at time t0
In case of contamination as initial condition: c(x, y, z, t = 0) = 0

## Slide 58: Embedding of a transport model in a flow model
Refined grid for the transport model within a coarse grid for the flow model.

## Slide 59: Solution methods for transport equation
Analytical solutions
Simple flow conditions / simple initial and boundary conditions, homogeneity
Neglecting diffusion/ dispersion
Pathlines, travel times, concentration along path lines
Numerical solutions
Grid methods: FD, FV, FE
Particle-tracking methods: MOC, Random-Walk

## Slide 60: Analytical solution
Instantaneous pollutant injection into parallel constant flow
Injection: t = 0, x = 0, y = 0

## Slide 61: Analytical solution
Permanent pollutant injection into parallel constant flow
Injection: t = 0, x = 0, y = 0

## Slide 62: Relation between flow and solute transport model
Note: In case of hydrodynamic inactive pollutants flow and transport processes are not coupled!
Schwartz et al. , 1983

## Slide 63: Numerical solutions
Grid Methods:
Finite Differences
Finite Elements
Finite Volumes
Particle-Tracking Methods:
Method of Characteristics (MOC)
Random-Walk-Method

## Slide 64: Problems: Numerical dispersion/ oscillations

## Slide 65: Rules for discretization
Courant-number:
Advection => small time steps required
Grid Peclet-number:
Dispersion => small grid sizes required

## Slide 66: Method of characteristics (MOC)
Basic idea: Divide the transport simulation in two half-steps. One step to calculate advection, and another step to calculate dispersion.
Calculate every step with the appropriate method. Advection by particle tracking, dispersion by grid methods.
Particles are necessary in every cell. The particles are indicators for the concentration in the cell. They are not particles with a mass!

## Slide 67: Random-walk-method
Basic idea: Divide the transport simulation in two half-steps. One step to calculate advection, and another step to calculate dispersion.
Compute advection and dispersion by particle tracking. Advection by integration of the velocity field, dispersion a random step.
In contrast to MOC particles posses a fixed mass. Many particles are required for the solution of the transport equation.

## Slide 68: Rules to avoid numerical problems
Discretization with grid Peclet numbers < 2
If this is not possible use MOC or random walk
Select time step such that Courant number < 1
Check results by grid refinement (grid convergence)

## Slide 69: Points of criticism of transport equation
Tailing is not reproduced (way out: e.g., double porosity)
Longitudinal dispersivity is not constant
The advection/dispersion equation is only a basic concept for complex processes
Up to now there is no acceptable and pragmatic alternative