## Slide 1: Hands-On Groundwater Modeling: Exercises Randolf Rausch & Anneli Guthke

## Slide 2: Exercise 1: Lens
Investigating the impact of contrasts in hydraulic conductivity on groundwater flow
(cf. Exercise 6.4 with ASM)

## Slide 3: Model setup
Steady state
Confined aquifer
Isotropic K
Aquifer thickness = 10 m
Discretization: ∆x = ∆y = 50 m
Determine spatial head distribution (hXY), streamlines and velocities for Tcentre = 0.1 m²/s (↑, Case 1) and 0.001 m²/s (↓, Case 2). Save and discuss the results.

## Slide 4: Results: Spatial head distribution and streamlines
Tcentre = 0.1 m²/s
Tcentre = 0.001 m²/s
Q = 0.075 m³/s
Q = 0.05 m³/s

## Slide 5: Lessons learned – capture zones
2 ∙ d
Quarry pond
Monitoring well

## Slide 6: Lessons learned – remediation problem
Stop
Low conductivity zones can cause very long remediation times of pump & treat measures
Source
Extraction well
Time
Concentration
(US EPA, 1997)

## Slide 7: Model setup
Steady state
Confined aquifer
Isotropic K
Aquifer thickness = 10 m
Discretization: ∆x = ∆y = 50 m , Nx = 21, Ny = 12
Now keep Tcentre = 0.001 (Case 2) m²/s, but set T = 0.0001 m²/s (Case 3). Compare to results of Case 1 and discuss.

## Slide 8: Lessons learned – boundary conditions
The resulting spatial head distribution only depends on the contrast between T and Tcentre !
This has implications for flow model calibration:
  Calibration = fitting model parameters to observed data (here: head)
  Without a flux boundary condition, calibration results (= optimal parameter values) will not be unique!
  To properly constrain a flow model, you need a flux measurement (which can be hard to obtain)
  Therefore very important: Check the water balance for plausibility!

## Slide 9: Model setup
Steady state
Confined aquifer
Isotropic K
Aquifer thickness = 10 m
Discretization: ∆x = ∆y = 50 m
Set T back to 0.01 m²/s and further reduce Tcentre to 0.00001 m²/s (↓↓, Case 4). Compare to Case 2 and discuss the result.

## Slide 10: Results: Sensitivity problem
                The detectable contrast in T is limited!
Tcentre = 0.001 m²/s
Tcentre = 0.00001 m²/s

## Slide 11: Exercise 2: Heterogeneous aquifer
How to average conductivities and fluxes in groundwater flow?
(cf. Exercise 6.3 with ASM)

## Slide 12: Model setup
Determine spatial head distribution (hXY), specific discharge (Q/A) and discharge (Q) for both cases. Discuss the result.
Determine the K-value for a homogeneous aquifer showing the same discharge (Q) for both cases.
h = 0.1 m
h = 0 m
h = 0.1 m
h = 0 m
0.35 m
0.3 m
0.35 m
Nx = 11, Ny = 20, m = 1 m

## Slide 13: Results: Spatial head distribution and discharge
Q = 3.7E-04 m³/s
Q = 1.37E-04 m³/s
Case A
Case B

## Slide 14: Average hydraulic conductivity – case A
Case A:
Darcy:
 Weighted arithmetic mean

## Slide 15: Average hydraulic conductivity – case B
Case B:
Darcy:
 Weighted harmonic mean

## Slide 16: Lessons learned – anisotropy

## Slide 17: Lessons learned – anisotropy
Sandstone Kh = 2.9E-05 m/s Kv = 2.4E-08 m/s
Limestone (low perm.) Kh = 7.4E-08 m/s Kv = 1.9E-09 m/s

## Slide 18: Lessons learned – scales
Simulation of 1 x 1 m domain or 1,000 x 1,000 m – does it make a difference?
Watch out for
  Subscale heterogeneities
  2D vs. 3D properties
  Upscaling of parameter values

## Slide 19: Lessons learned – averaging conductivities
Zones parallel to flow direction: weighted arithmetic mean
Zones perpendicular to flow direction: weighted harmonic mean
Averaging K-values within one zone: ???
Depends on your assumption how K-values are distributed on that scale

## Slide 20: Lessons learned – averaging conductivities
For a log-normal distribution of values: Geometric mean
Rupp et al, 2011

## Slide 21: Lessons learned – averaging conductivities
Connection with non-log-transformed values:
Geometric mean = „averaging of orders of magnitude“
Samples | i=1 | i=2 | i=3 |  | arithm. mean | harm. mean | geom. mean
K [m/s] | 1,0E-03 | 1,0E-04 | 1,0E-05 |  | 3,7E-04 | 2,7E-05 | 1,0E-04
Y=ln(K) [-] | -6,91 | -9,21 | -11,51 |  | -9,21 | - | -

## Slide 22: Exercise 3: Excavation pit
How to design the dewatering of an excavation pit?
(cf. Exercise 6.10 with ASM)

## Slide 23: Model setup
PLAN VIEW
5 m
3 m
Determine the amount of water that flows into the excavation pit, the catchment area and the fraction of water coming from the river under stationary conditions.
Unconfined aquifer
Aquifer bottom at z = 0
GWR = 189 mm/a
K = 1E-03 m/s

## Slide 24: Model grid
How could you check whether the right-hand boundary is far enough to not affect your results?
2,000 m (40 cells)
900 m (19 cells)
Δx = Δy = 50 m

## Slide 25: Results: Spatial head distribution
½ Qexcavation pit = -0.0129 m³/s ½ Qriver = 0.0068 m³/s

## Slide 26: Model setup
PLAN VIEW
5 m
3 m
Give a recommendation for the pumping rate of the wells. How long do we need to pump to achieve a water-free excavation pit?
dexcavation pit = 25 m
dwells = 50 m
Unconfined aquifer
Aquifer bottom at z = 0
GWR = 189 mm/a
K = 1E-03 m/s
Transient conditions
S = 0.1

## Slide 27: Initial conditions

## Slide 28: Model setup
Q = 8 x -0.0024 m³/s = -0.0192 m³/s
Monitoring well at x = 50 m and y = 300 m
and x = 0 m and y = 250 m
Simulation time of 400 days, 50 time steps, time step multiplier = 1.2

## Slide 29: Results: Spatial head distribution

## Slide 30: Results: Head time series
3 m
93 days

## Slide 31: Exercise 4: Pumping well catchment
Determining the catchment area of a well
(cf. Exercise 6.17 with ASM)

## Slide 32: Model setup
PLAN VIEW
Determine the catchment area and the 365 days-line of the well.
Confined aquifer
Aquifer bottom at z = 0
GWR = 252 mm/a
T = 5E-03 m²/s
m = 10 m
nf = 0.1
Q = 5 l/s
10 m
u

## Slide 33: Model grid
2,500 m (50 cells)
2,550 m (51 cells)
Δx = Δy = 50 m
(29, 26)

## Slide 34: Results: Spatial head distribution

## Slide 35: Results: Pumping well catchment

## Slide 36: Results: Isochrones

## Slide 37: Exercise 5: River leakage
Investigate the impact of river in-/exfiltration on groundwater flow
(cf. Exercise 6.7 with ASM)

## Slide 38: Model setup
8 m
10 m
Determine the piezometric head distribution and the water balance under steady state conditions. Interpret the results.
Unconfined aquifer
Aquifer bottom at z = 0
K = 1E-02 m/s
Width of river w = 50 m
River bottom 3 m below river stage
River bed colmation  Leakage factor l = 5E-06 1/s
1,550 m
950 m
10 m
8 m

## Slide 39: Model grid
Δx = Δy = 50 m
1,550 m (32 cells)
950 m (19 cells)

## Slide 40: River leakage in Modflow
Modflow requires the river stage hr, river bottom br and the riverbed conductance (CRIV)
The riverbed conductance is defined as: , with
CRIV = hydraulic conductance of riverbed (L2/T)
K = hydraulic conductivity of the riverbed (L/T)
L = length of the river within a cell (L)
W = width of the river within a cell (L)
M = thickness of the river bed (L)
K/M = leakage factor (1/T)

## Slide 41: Results: Spatial head distribution
Identify areas of infiltration to the groundwater and exfiltration from the groundwater!

## Slide 42: Results: Water budget
Q_infiltration = 0.0728 m³/s, Q_exfiltration = 0.0732 m³/s. What is the reason for the slight asymmetry?

## Slide 43: Exercise 6: Time-variant recharge
Determine time-variant groundwater flow under varying recharge rates
(cf. Exercise 6.20 with ASM)

## Slide 44: Model setup
10 m, perfect hydraulic coupling
Determine the time series of piezometric head at the three observation wells. Repeat the calculation with Sy = 0.01. Compare and interpret the results.
Confined aquifer
Aquifer thickness m = 10 m
T = 5E-03 m²/s
Transient conditions
Storage coeff. S = 0.001
Average GWR = 4 l/(s km²)
2,100 m
1,100 m

## Slide 45: Model grid
2,100 m (21 cells)
1,100 m (11 cells)
Δx = Δy = 100 m
OW1 (450/550)
OW2 (1,050/550)
OW3 (1,650/550)

## Slide 46: Time-variant groundwater recharge
Simulation time of 370 days, 37 stress periods with time step length of 10 days.

## Slide 47: Initial conditions

## Slide 48: Results: Head time series
S = 0.001
Amplitude depends on distance from river boundary condition!

## Slide 49: Results: Head time series
S = 0.01
Amplitude depends on storage coefficient (and transmissivity): repeat with varied ratios of T/S!

## Slide 50: Exercise 7: Parameter calibration
Determine optimal (most realistic) transmissivity values from observed head data

## Slide 51: Model setup
Calibrate the 3 transmissivities such that the observed head data are reproduced. Start with T = 0.01 m²/s for all three zones. Compute the steady state head distribution and the catchment area of the well with optimized transmissivities.
Confined aquifer
Aquifer top = 0 m
Aquifer bottom = -50 m
3 zones of homogeneous T
Steady state conditions
GWR = 5E-09 m³/(s∙m²)
Well pumping rate = 0.03 m³/s

## Slide 52: Model grid
10 m
Observed heads:
h1(850/1,950) = 11.41 m
h2(2,750/1,950) = 10.20 m
h3(2,050/550) = 11.93 m
h4(150/150) = 13.67 m
h5(3,050/450) = 11.51 m
h6(3,650/1,350) = 10.08 m
h7(450/2,650) = 11.52 m
4,000 m (80 cells)
3,000 m (60 cells)
∆x = ∆y = 50 m
Well (2,925/1,825)

## Slide 53: Parameter zonation
4,000 m (80 cells)
3,000 m (60 cells)
T1
T2
T3

## Slide 54: Results: Scatter diagram before, ...

## Slide 55: Results: ... during...

## Slide 56: Results: ... and after calibration

## Slide 57: Results: Head distribution and well catchment

## Slide 58: Exercise 8: Solute transport
Determine the contaminant plume resulting from a permanent point-source injection into a steady state flow field

## Slide 59: Flow model setup
First, determine the steady-state flow field as a basis for the transport model.
Flow:
Confined aquifer
Aquifer thickness m = 10 m
Isotropic transmissivity T = 1.2E-02 m²/s
Steady state conditions
h = 0.3 m
h = 0 m
300 m
170 m

## Slide 60: Model grid
Observation wells:
OW1 (145 m / 85 m)
OW2 (195 m / 85 m)
OW3 (245 m / 85 m)
31 cells
17 cells
∆x = ∆y = 10 m
Injection
(95 m / 85 m) = (10/9)

## Slide 61: Results: Steady-state flow field

## Slide 62: Transport model setup
Compute the development of the contaminant plume for 400 days. Compare the breakthrough curves [mg/l] at the three observation wells and visualize the spatial distribution of concentration levels at steady-state conditions.
Transport:
Effective porosity nf = 0.1
Conservative tracer (no adsorption, no decay)
Longitudinal dispersivity αL = 10 m
Transverse dispersivity αT = 1 m
Injection rate M = 1 kg/d

## Slide 63: Results: Breakthrough curves

## Slide 64: Results: Contaminant plume evolving over 400 days

## Slide 65: Summary / Lessons learned
Exercises:
  Lens (steady state, confined aquifer)
  Heterogeneous aquifer (steady state, confined aquifer)
  Excavation pit (steady state/transient, unconfined aquifer)
  Well catchment (steady state, confined aquifer)
  River leakage (steady state, unconfined aquifer)
  Time-variant groundwater recharge (transient, confined aqu.)
  Calibration (steady state, confined aquifer)
  Solute transport (steady state flow/transient transport, confined aquifer)

## Slide 66: Aquifer types
Confined aquifers:
  User specified transmissivity and storage coefficient
Unconfined aquifers:
  Calculated transmissivity -> specify hydraulic conductivity
  Specific yield

## Slide 67: Time parameters
For steady state calculations:
  No specification of total time
  Storage coefficient, … not needed
  Initial conditions are only relevant for the iterative solver
For transient conditions:
  Specify total time and time steps in correct units
  Assign meaningful initial conditions (e.g., from steady-state calculation)
  Make sure that you look at the results of the intended time step!

## Slide 68: Boundary conditions
Dirichlet (1st type): prescribed head
Neumann (2nd type): specified flux
Cauchy (3rd type): leakage
Investigate and understand the impact of the chosen boundary conditions on modeling results (and, e.g., calibration strategy)

## Slide 69: Model setup
Watch out for units – be consistent throughout the whole data input process!
Check the units that the program expects
Examples:
  Transmissivity [e.g., m²/s]
  Well abstraction rates [ m³/s]
  Recharge rates [ m/s]

## Slide 70: Model calibration
From Dirichlet boundary conditions, only contrasts in T can be identified (to some degree)
To calibrate absolute values of T, you need a specified flux!
Document each change in model parameters and the resulting changes in model results properly
Perform a systematic sensitivity analysis

## Slide 71: Plausibility checks for model results
Interpret the water budget
Interpret piezometric head distribution, velocity vectors and streamlines (they have to „match“!)

## Slide 72: Averaging of fluxes
Zones of different transmissivity parallel to flow direction: arithmetic mean
Zones of different transmissivity perpendicular to flow direction: harmonic mean (zero flux constraint!)
Anisotropy: vertical conductivity typically much lower than horizontal conductivity